## Slide 1
Water-quality changes across sampling taps
Team 7 • Ideation • SDG 6: Clean Water and Sanitation
Problem: small water-quality changes can be hard to resolve across multiple taps.
User: a treatment or reuse operator deciding when to investigate a change.
SDG 6.3: improve water-quality monitoring and support safer reuse decisions.
SDG 6.4: potential water-efficiency benefit; water saved is not yet measured.
TEAM 7 • IDEATION / SIMULATION
1 / 5
Notes: Proposed use case; no verified customer or quantified missed-event prevalence. United Nations target definitions: https://sdgs.un.org/goals/goal6 and https://unstats.un.org/sdgs/metadata/?Goal=6&Target= . Target6.3 concerns water quality, pollution reduction, wastewater treatment and safe reuse; target6.4 concerns water-use efficiency and sustainable withdrawals. Our proposed contribution is monitoring, not proven delivery of either target. This is a salt-proxy change detector, not a drinking-water safety test. The supplied template explicitly distinguishes October ideation from the in-person presentation; this concise artifact is created at the user’s request. Working nameTeam7 confirmed; final name and roster remain unconfirmed.

## Slide 2
Proposed solution: correlated optical sensing
Squeezed light → water taps → homodyne readout → mean-change estimate
Measure dissolved-salt changes through refractive index at 1550 nm.
Distribute one squeezed mode: correlated noise cancels partly in the mean.
Estimate q̂ = Σ yᵢ / M with a classical Gaussian model and linear estimator.
Quantum sensing advantage is proposed; no quantum-computing speedup is claimed.
TEAM 7 • IDEATION / SIMULATION
2 / 5
Notes: Technical rigor: 30%. Classical matrix operations and Gaussian threshold tests; no quantum computing speedup, QAOA, VQE or QML execution. Covariance is propagated through loss and phase jitter. Objective is minimum error for an unbiased arithmetic-mean estimate under the stated resource constraints; no changing site weights to discard noisy nodes. Theory https://arxiv.org/abs/1711.10459 and https://doi.org/10.1103/PhysRevResearch.2.023030 . Classical estimator is computationally tractable. QC-specific eligibility must be confirmed with organizers. Hack stack: Python, NumPy, SciPy, Matplotlib. No quantum hardware has been built.
NaCl calibration: Saunders https://doi.org/10.1364/AO.55.000947 . Around500mg/kg, dn/dc=1.6207394e-7 RIU/(mg/kg). Effective length10µm is assumed, giving6.5699393e-6rad/(mg/kg). Local concentrations may differ. NaCl-equivalent mg/kg is a nonspecific proxy: no arsenic/nitrate selectivity or mg/L conversion. Classical simulator uses Python, NumPy and SciPy. Hardware remains proposed. Product concept: calibrated optical sampling module with operator software and confirmatory chemical analysis. Quantum-computing emphasis of rubric remains an eligibility question.

## Slide 3
Simulation design and evidence
Continuous-variable optics • Continuous monitoring • Matched probe photons
Baselines: coherent light, independent squeezing and optimized classical power.
Experiments: 1–64 taps; fiber loss, thermal drift, power and synthetic events.
Published anchors: NaCl response, fiber attenuation and demonstrated squeezing.
Assumed pilot: 16 taps, 100 m links, 10 nW/tap, 1 s windows, 50 µK residual.
TEAM 7 • IDEATION / SIMULATION
3 / 5
Notes: NaCl: Saunders https://doi.org/10.1364/AO.55.000947 ; squeezing Mehmet https://arxiv.org/abs/1110.3737 ; fiber https://www.corning.com/media/worldwide/coc/documents/Fiber/application-notes/AN2008.pdf ; thermo-optic Kim https://opg.optica.org/abstract.cfm?uri=sensors-2012-STu1F.3 . Supplied Dowran https://doi.org/10.1364/OPTICA.5.000628 reports795nm199kHz air sensitivities8.6/6.8/5.5e-10RIU/sqrtHz; not transferable to1s1550nm water. Supplied Pooser/Lawrie PDF is supporting information of a separate paper. QML https://doi.org/10.3390/quantum8030060 ; matched RBF remains strong. Complete sources and each config parameter in docs/PROJECT_REPORT.md AppendixA.
Pilot eta=.731827,sourceNs1.6 photons/mode,9.18dB squeezing; source cap10dB and mode rate1MHz are engineering targets. Equal launched carrier+squeezed photons, excluding pump and LO electricity. Nearest64distinct supplied USGS-labelled coordinates; route1.3×greatcircle, not surveyed fiber. Sweep includes10mK stress case and1nW–70µW classical power. Ideal lossless uncapped fitM33–64 yields−.953 vs−.500 RMS slope only with growing total squeezing; no deployable1/M claim.13internal model tests;100000 null/alternative draws per strategy verify Gaussian ROC. No field data are generated or claimed; see docs/PROJECT_REPORT.md.

## Slide 4
Current result: 28% lower modeled error
Controlled 16-tap pilot • Differential NaCl-equivalent concentration
Chart: Probe strategy
| Coherent | Independent squeezed | Distributed squeezed
Optical error | 0.079619 | 0.064733 | 0.047583
Total error | 0.092101 | 0.079585 | 0.066389
Total RMSE: 0.0921 → 0.0664 mg/kg; optical precision improves 1.67×
64-site gain is only 1.11×; at 10 mK drift, useful advantage disappears
TEAM 7 • IDEATION / SIMULATION
4 / 5
Notes: Quantum justification: 20%. This is a prediction for a proposed controlled instrument, not a measured water sensor. Optical RMSE .079619 vs .047583; total precision gain 1.387×. The ambitious common temperature residual is an engineering assumption. Probe photon accounting includes squeezed photons deducted from carrier power, but excludes pump and local oscillator energy.
results/summary.json pilot16. No measured-field accuracy claim. Common residual 50 microkelvin is an ambitious compensated bench target.
Results/summary.json gives27.92% RMSE reduction versus coherent and16.58% versus independent squeezing. At64regional sites compare optimized coherent .0728867 to distributed .0655362mg/kg.10mK residual gives approximately9.137mg/kg for either strategy. More classical power also shrinks total gain. These are conditional predictions, not measured hardware results or experimental proof of the literature. Source plot uses exact model results rounded for spreadsheet portability.

## Slide 5
Impact, sustainability and next steps
Three measurable KPIs • A laboratory pilot before deployment
Estimation: 28% lower simulated RMSE at the same launched probe-photon budget.
Monitoring: step detection 24% → 47% at 1% false alarm per decision; no liters saved yet.
Resources: 160 nJ probe/window for both; total energy and cost remain unmeasured.
Next: calibrate one cell, test four taps blindly, then measure energy and alarm rates.
TEAM 7 • IDEATION / SIMULATION
5 / 5
Notes: Required closing three claims from judging guidance. All pilot claims use16nodes,10nW/node,1s,50µK common residual. Detection uses.15mg/kg increase and1% false alarm per decision. Optical energy160nJ is equal resources, not measured sustainability improvement. Algorithm is estimator accuracy, not quantum computational runtime. Next KPI: total joules per validated useful detection at matched coverage, false-alarm rate and response time. Results do not prove/disprove literature: conditional model consistency only.
Detection of.15mg/kg mean increase,16nodes,1s,50µK residual.1% per-window false alarm at1Hz gives36expected flagged windows/hour; not an operational alarm policy. Need a separately validated sequential rule. First audience controlled plant lab; possible model research pilot then monitoring module, no confirmed partner or revenue. Compare conventional conductivity and higher-power coherent optics. Expansion only if useful detection beats these alternatives under an operator-relevant constraint and measured total cost/energy. Seek water operator and optical laboratory for a scoped pilot. Figures do not prove/disprove experimental literature; they show conditional consistency and failure regimes. Sources and technical details in docs/PROJECT_REPORT.md and results/summary.json. The proposed environmental impact remains unvalidated.